## Slide 1: An Introduction to Beluga
Sean Matthew Nolan

## Slide 2: Overview
Introduction
  Indirect vs. Direct Optimization
Solver Description
  Algorithmic Overview
  Indirect Optimization
  Continuation Methods
  BVP Solving
Examples
  Brachistochrone Problem with Input Details
  Planar Hypersonic Problem
  3DOF Hypersonic Problem
  Estimation Problems
Conclusion

## Slide 3: Introduction
Beluga is a optimization framework for optimal control problems (OCP)
  Python 3.5+
  Available with MIT License from
    https://github.com/Rapid-Design-of-Systems-Laboratory/beluga
    PyPI with pip install beluga
  Documentation: https://beluga.readthedocs.io/en/latest/
Practically only publicly available solver capable of solving problems using indirect methods
Abstracts and automates optimization process for user

## Slide 4: Optimization Techniques
Direct Methods
  Discretize a problem's state and control variables and then adjusts them directly to minimize the objective function
  Advantages:
    Simpler for user to pose problem
    Many solvers available
Indirect Methods
  Apply optimal control theory to find the optimally conditions in terms of adjoint differential equations (costates), minimum principle, and boundary conditions
  Advantages:
    Result in high quality solutions
    Computational benefits: parallelizable, mitigated curse of dimensionality, fewer numerical artifacts, dynamics always enforced

## Slide 5: Software Available for Optimal Control
Name | Method
GPOPS (I and II) | Direct
DIDO | Direct
OTIS | Direct
POST (I and II) | Direct
PSOPT | Direct
PROPT | Direct
Name | Method
DIRCOL | Direct
Various STK propagators | Direct
OptimTraj | Direct
opty | Direct
OpenGoddard | Direct
dynopt | Direct
Name | Method
FROST | Direct
GESOP/Astos | Direct
SOCS | Direct
HamPath* | Indirect
OCCAL** | Indirect
beluga*** | Indirect
* HamPath does not perform dualization. The user is required to do it manually
** Other than a single 1994 publication, OCCAL is nonexistent
*** The solver of explained here

## Slide 6: Beluga Details

## Slide 7: Beluga Flowchart
Form BVP
Form Initial Guess
Continuation Handling
Solve Latest BVP
Final BVP?
Input OCP
Solutions
No
Yes
Form BVP: Boundary value problem is formed with optimal control theory (indirect) or arranged as parameter optimization problem (direct)
Continuation: Solver solves problem with difficult-to-solve BC values, constants, constraints, etc. by “stepping” toward it using easier-to-solve problems as guesses for more difficult ones
Solve BVP: The BVP for that continuation step is solved using a shooting or collocation method

## Slide 8: Expanded Beluga Flowchart with Shooting Method
Start
End
Form Necessary Conditions using OCT
Initialize Continuation Process
Converged?
Solve TPBVP using Shooting Method/Newton Method Root Solving
Set BCs for Next Continuation Step
Propagate Trajectory and STM Forward
Form Initial Guess
Set Guess for Initial States from Previous Solution
Scale Problem
Check BCs Residuals
Apply Corrections using STM
Cont. Done?
Continuation Handling
OCT and
Initialization
Yes
Yes
No
No

## Slide 9: Optimal Control Problem
An optimal control problem is given by
Subject to dynamics:
And initial and terminal BCs:

## Slide 10: Indirect Optimization
Augmenting cost functional with dynamics, initial, and terminal constraints ( are costates)
For convivence, define Hamiltonian
The optimal solution requires that the first variation ()is zero

## Slide 11: Indirect Optimization
Integration by parts and noting and eliminates dependency on
From above, the necessary conditions are derived:
; ;
Minimum principle used if above not sufficient:

## Slide 12: Continuation Method
Optimal control problems, particularly with indirect methods, are numerically sensitive and have small radius of convergence
Problems with difficult-to-solve BC values, constants, constraints, etc. need a sufficiently “close” guess
An easier to solver problem can be used as a guess for the harder one
The continuation sequentially solves more difficult problems using last solution as the guess for the current one

## Slide 13: Solving BVP
Collocation
  Discretize trajectory into discrete nodes
  Repose dynamics as constraints between nodes
  Adjust state values at nodes until constraints satisfied
Shooting Methods
  Propagates trajectory and STM using guess for initial conditions
  Computes terminal BC error
  Adjusts initial guess using linearized sensitivities from STM based on error

## Slide 14: Examples

## Slide 15: Brachistochrone Problem
Objective:
Minimum Time:
Control:
Slope Angle Below Horizon:
Dynamics:

## Slide 16: Brachistochrone Input
Import beluga and pyplot | import beluga import matplotlib.pyplot as plt
Initialize OCP object | ocp = beluga.OCP('brachisto’)
Define independent variable with unit | ocp.independent('t', 's')
Define states with corresponding EOM and units | ocp.state('x', 'v*cos(theta)', 'm') \ .state('y', 'v*sin(theta)', 'm') \ .state('v', 'g*sin(theta)', 'm/s')
Define control with unit | ocp.control('theta', 'rad')
Define constant in dynamics Define and in BCs | ocp.constant('g', -9.81, 'm/s^2') ocp.constant('x_f', 0, 'm') ocp.constant('y_f', 0, 'm')
Add minimal time cost | ocp.path_cost('1', '1')
Add initial point BCs Add terminal point BCs | ocp.constraints() \ .initial('x', 'm') \ .initial('y', 'm') \ .initial('v', 'm/s') \ .terminal('x - x_f', 'm') \ .terminal('y - y_f', 'm')
Input reference values for scaling | ocp.scale(m='y', s='y/v', kg=1, rad=1, nd=1)
Import beluga and pyplot | import beluga import matplotlib.pyplot as plt
Initialize OCP object | ocp = beluga.OCP('brachisto’)
 | ocp.independent('t', 's')
 | ocp.state('x', 'v*cos(theta)', 'm') \ .state('y', 'v*sin(theta)', 'm') \ .state('v', 'g*sin(theta)', 'm/s')
 | ocp.control('theta', 'rad')
 | ocp.constant('g', -9.81, 'm/s^2') ocp.constant('x_f', 0, 'm') ocp.constant('y_f', 0, 'm')
 | ocp.path_cost('1', '1')
 | ocp.constraints() \ .initial('x', 'm') \ .initial('y', 'm') \ .initial('v', 'm/s') \ .terminal('x - x_f', 'm') \ .terminal('y - y_f', 'm')
Input reference values for scaling | ocp.scale(m='y', s='y/v', kg=1, rad=1, nd=1)

## Slide 17: Brachistochrone Input
Input algorithm used for solving BVP (Shooting with Armijo line-search root solving) | bvp_solver = beluga.bvp_algorithm('Shooting', algorithm='Armijo')
Set guess generator to propagate initial short guess using given and control | guess_maker = beluga.guess_generator( 'auto', start=[0, 0, 0], # Starting values for states in order costate_guess=-0.1, control_guess=[-3.14159265/2], use_control_guess=True)
Initialize and define continuation set to linearly step to trajectory with in 6 steps | continuation_steps = beluga.init_continuation() continuation_steps.add_step('bisection’) \ .num_cases(6) \ .const('x_f', 10) \ .const('y_f', -10)
Solve problem with indirect methods, scaling, and saving output | sol_set = beluga.solve( ocp=ocp, method='indirect', bvp_algorithm=bvp_solver, steps=continuation_steps, guess_generator=guess_maker, autoscale=True, save='brachisto.beluga')
Plot result with pyplot | plt.plot(sol_set[-1][-1].y[:, 0], sol_set[-1][-1].y[:, 1]) plt.title('Brachistochrone Problem') plt.xlabel('$x$ [m]') plt.ylabel('$y$ [m]') plt.show()
Input algorithm used for solving BVP (Shooting with Armijo line-search root solving) | bvp_solver = beluga.bvp_algorithm('Shooting', algorithm='Armijo')
 | guess_maker = beluga.guess_generator( 'auto', start=[0, 0, 0], # Starting values for states in order costate_guess=-0.1, control_guess=[-3.14159265/2], use_control_guess=True)
 | continuation_steps = beluga.init_continuation() continuation_steps.add_step('bisection’) \ .num_cases(6) \ .const('x_f', 10) \ .const('y_f', -10)
Solve problem with indirect methods, scaling, and saving output | sol_set = beluga.solve( ocp=ocp, method='indirect', bvp_algorithm=bvp_solver, steps=continuation_steps, guess_generator=guess_maker, autoscale=True, save='brachisto.beluga')
Plot result with pyplot | plt.plot(sol_set[-1][-1].y[:, 0], sol_set[-1][-1].y[:, 1]) plt.title('Brachistochrone Problem') plt.xlabel('$x$ [m]') plt.ylabel('$y$ [m]') plt.show()

## Slide 18: Planar Hypersonic Problem
Objective:
Max Energy:
Control:
Angle of Attack:
Dynamics:

## Slide 19: Hypersonic 3DOF Problem
Objective:
Max Energy:
Control:
Angle of Attack:
Bank Angle:
Dynamics:

## Slide 20: Navigation Based Path Planning
Optimal Control Theory used to minimize state estimation errors of a vehicle

## Slide 21: Aircraft Estimation Problem
Objective:
Control:
Measurement:

## Slide 22: Aircraft Estimation Problem
Vehicle performs “S-curve” maneuvers similar to those in previous studies
Variance reduced from 67.7 m2 to 48.3 m2 (28.6% reduction)

## Slide 23: Conclusion
Beluga provides an automated framework for solving optimal control problems using indirect methods
Available with MIT License from
  https://github.com/Rapid-Design-of-Systems-Laboratory/beluga
  PyPI with pip install beluga
Documentation: https://beluga.readthedocs.io/en/latest/
Anyone can use and contribute!